## Slide 1: Instruction Set of 8085
Click to add text

## Slide 2: Introduction
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions.

## Slide 3
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or Instruction Byte.

## Slide 4: Classification of Instruction Set
Data Transfer Instruction
Arithmetic Instructions
Logical Instructions
Branching Instructions
Control Instructions

## Slide 5: Syntax

## Slide 6: Data Transfer Instructions
These instructions move data between registers, or between memory and registers.
These instructions copy data from source to destination.
While copying, the contents of source are not modified.

## Slide 7: Data Transfer Instructions
This instruction copies the contents of the source register into the destination register.
The contents of the source register are not altered.
If one of the operands is a memory location, its location is specified by the contents of the HL registers.

## Slide 8: Data Transfer Instructions

## Slide 9: Data Transfer Instructions

## Slide 10: Data Transfer Instructions
The 8-bit data is stored in the destination register or memory.
If the operand is a memory location, its location is specified by the contents of the H-L registers.
Example: MVI E, 1AH or MVI M, 2BH

## Slide 12: Data Transfer Instructions
Example: LDAX B
The contents of the designated register pair (BC) point to a memory location.
This instruction copies the contents of that memory location into the accumulator.
The contents of either the register pair or the memory location are not altered.

## Slide 13: Data Transfer Instructions
This instruction loads 16-bit data in the register pair.
Example: LXI H, 2034 H

## Slide 14: Data Transfer Instructions
This instruction copies the contents of memory location pointed out by 16-bit address into register L.
It copies the contents of next memory location into register H.
Example: LHLD 2040 H

## Slide 15: Data Transfer Instructions
The contents of accumulator are copied into the memory location specified by the operand.
Example: STA 2500 H

## Slide 16: Data Transfer Instructions
The contents of accumulator are copied into the memory location specified by the contents of the register pair.
Example: STAX B
Suppose, (B)=20H, (C)=01H
(A)-(M)2001H

## Slide 17: Data Transfer Instructions
The contents of register L are stored into memory location specified by the 16-bit address.
The contents of register H are stored into the next memory location.
Example: SHLD 2550 H

## Slide 18: Data Transfer Instructions
The contents of register H are exchanged with the contents of register D.
The contents of register L are exchanged with the contents of register E.
Example: XCHG

## Slide 19: Data Transfer Instructions
The contents of registers H and L are copied into the program counter (PC).
The contents of H are placed as the high-order byte and the contents of L as the low-order byte.
Example: PCHL

## Slide 20: Data Transfer Instructions
This instruction loads the contents of H-L pair into SP.
Example: SPHL

## Slide 21: Data Transfer Instructions
The contents of I/O port are copied into accumulator.
Example: IN 8C H

## Slide 22: Data Transfer Instructions
The contents of accumulator are copied into the I/O port.
Example: OUT 78 H

## Slide 23: Arithmetic Instructions
These instructions perform the operations like:
  Addition
  Subtraction
  Increment
  Decrement

## Slide 24: Addition
Any 8-bit number, or the contents of register, or the contents of memory location can be added to the contents of accumulator.
The result (sum) is stored in the accumulator.
No two other 8-bit registers can be added directly.
Example: The contents of register B cannot be added directly to the contents of register C.

## Slide 25: Subtraction
Any 8-bit number, or the contents of register, or the contents of memory location can be subtracted from the contents of accumulator.
The result is stored in the accumulator.
Subtraction is performed in 2’s complement form.
If the result is negative, it is stored in 2’s complement form.
No two other 8-bit registers can be subtracted directly.

## Slide 26: Increment / Decrement
The 8-bit contents of a register or a memory location can be incremented or decremented by 1.
The 16-bit contents of a register pair can be incremented or decremented by 1.
Increment or decrement can be performed on any register or a memory location.

## Slide 27: Arithmetic Instructions

## Slide 28: Logical Instructions
These instructions perform various logical operations with the contents of the accumulator.

## Slide 29: Branching Instructions
This group of instructions alters the sequence of program execution either conditionally or unconditionally

## Slide 30: Jump Conditionally

## Slide 31: Branching Instructions
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Before the transfer, the address of the next instruction after CALL (the contents of the program counter) is pushed onto the stack.
Example: CALL 2034 H.

## Slide 32: Branching Instructions
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand based on the specified flag of the PSW.
Before the transfer, the address of the next instruction after the call (the contents of the program counter) is pushed onto the stack.
Example: CZ 2034 H.

## Slide 33: Call Conditionally

## Slide 34: Branching Instructions
The program sequence is transferred from the subroutine to the calling program.
The two bytes from the top of the stack are copied into the program counter, and program execution begins at the new address.
Example: RET.

## Slide 35: Branching Instructions
The program sequence is transferred from the subroutine to the calling program based on the specified flag of the PSW.
The two bytes from the top of the stack are copied into the program counter, and program execution begins at the new address.
Example: RZ.

## Slide 36: Return Conditionally

## Slide 37: Branching Instructions
The RST instruction jumps the control to one of eight memory locations depending upon the number.
These are used as software instructions in a program to transfer program execution to one of the eight locations.
Example: RST 3.

## Slide 38: Restart Address Table

## Slide 39: Machine Control Instructions
These instructions control machine functions such as Halt, Interrupt, or do nothing.