## Slide 1: Method of Data transfer in 8085 Microprocessor

## Slide 2: Data Transfer Mechanism
Data Transfer can take place between processor-memory, processor-I/O devices , and memory-I/O devices
The mechanism differs based on characteristics such as:
  Addressing of the device
  Amount of data transferred
  Method of data transfer
  Interaction among devices

## Slide 3
  Based on Addressing of the device
    I/O Mapped data transfer Memory Mapped data transfer
    Based on program and hardware involved
              Programmed Data Transfer
Polled mode Interrupt driven
Direct Memory Access
Burst mode Cycle stealing mode

## Slide 4
Based on Method of data transfer and access
Parallel data transfer
Simple mode Handshake mode
Serial Data Transfer
Synchronous Asynchronous

## Slide 5: I/O mapped and Memory mapped Data transfer
In I/O mapped data transfer method, I/O devices and memory are handled separately.
A separate address range is assigned for I/O devices and separate control signals are used for memory access and I/O device read/write operation
Separate instructions are used for input and output device access (IN and OUT instructions)
A single address can be assigned to both I/O and memory location

## Slide 6
In memory mapped data transfer, each I/O device is treated like a memory location.
The control signals are used for memory access and I/O device read/write operation.
Each input or output device is identified by a unique address in the memory address range.
Maximum memory addressing capacity is reduced

## Slide 7: Programmed Data Transfer
The instructions for programmed data transfer is written and controlled by programmer
The transfer between processor and I/O devices (vice versa) takes place by executing the corresponding instruction.
Based on time of execution, it is divided in to
  Polled mode
  Interrupt driven

## Slide 8: Polled Mode
  In Polled mode data transfer, data is read from an input device when the processor is ready.
  If the input device is not ready, the processor waits till the device is ready with data
  Similarly, data is written in to output device by the processor, when it executes the write instruction corresponding to that output device.
  Considerable wastage of processor time in waiting.

## Slide 9: Interrupt Driven Data Transfer
Interrupt is a process where an external device can get the attention of the microprocessor.
An interrupt is considered to be an emergency signal that may be serviced.
  The Microprocessor may respond to it as soon as possible.
Interrupts are useful when interfacing I/O devices with low data-transfer rates, like a keyboard or a mouse, in which case polling the device wastes valuable processing time

## Slide 10: Interrupt Driven Data Transfer
In interrupt driven data transfer, data is read from an input device only when it is ready with data.
When the device is ready, it gives an interrupt signal to the processor.
In the Interrupt service routine (ISR), a program is executed to read the data from the corresponding input device

## Slide 11
The data transfer is done only when the device is ready. The processor need not wait, can execute other main routines
Suitable for slow I/O devices

## Slide 12
Programmed I/O and interrupt I/O provide data transfer between the Microprocessor and external devices.
However, there are various instances when data must be moved between memory and external devices.

## Slide 13: Direct Memory Access (DMA)
DMA is an input output technique used for high speed data transfer
Large block of data transfer between system memory and I/O
It introduces two new signals that are
  HOLD
  HLDA

## Slide 14
DMA performs data transfer memory and an external device without involving the CPU.
The interface or controller chip must be perform memory read and write operations in similar way as microprocessor.
DMA data transfer can be of 2 types:
  Burst or block transfer mode
  Cycle stealing or interleaved mode

## Slide 15
In bust mode of DMA data transfer, a complete block of data is transferred in a single DMA cycle
The system bus is released by the DMA controller when the required bytes of data are transferred.

## Slide 16
In cycle stealing mode of DMA data transfer, a bock of data is transferred in many DMA cycles.
The system bus is released to the processor after a set of bytes are transferred in one DMA cycle.
The processor is not halted for a long time.

## Slide 17: Parallel Data Transfer
In Parallel mode of data transfer, all the bits in a word are simultaneously transmitted.
Not suitable for long distance transfers
Can be of two types
  Simple or synchronous mode
  Handshake mode

## Slide 18
In simple mode of data transfer, data is read from an input device by the processor irrespective of the status of the device.
  Similarly, data is written in to an output device irrespective of the status of the device.
In handshake mode, the processor checks the status of I/O device before transmission.

## Slide 19: Serial data transfer
Only one bit is transferred at a time
Is a low cost way to send data over long distance
All the bits in a data word can be transmitted by using a shift register and transferring the data bit by bit.
Can be done in 2 ways
  Synchronous
  Asynchronous

## Slide 20
  In Synchronous data transfer, the sending and receiving device are synchronized with a common clock.
    Data transfer takes place with a fixed and known time frame
In asynchronous data transfer, the data words are transmitted with a random time frame between them.