## Slide 1: Addressing Modes of 8085

## Slide 2: Introduction
Instruction set is the collection of all groups of instructions. (8085 has 246 instructions).
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or Instruction Byte.
The source and destinations of data is known as operand

## Slide 3: Introduction
To perform any operation, we have to give the corresponding instructions to the microprocessor.
In each instruction, programmer has to specify 3 things:
  Operation to be performed.
  Address of source of data.
  Address of destination of result

## Slide 4: Addressing Modes of 8085
The method by which the address of source of data or the address of destination of result is given in the instruction is called Addressing Modes.
The term addressing mode refers to the way in which the operand of the instruction is specified.

## Slide 5: Types of Addressing Modes
Intel 8085 uses the following addressing modes:
  Direct Addressing Mode
  Register Addressing Mode
  Register Indirect Addressing Mode
  Immediate Addressing Mode
  Implicit Addressing Mode

## Slide 6: Direct Addressing Mode
In this mode, the address of the operand is given in the instruction itself

## Slide 7: Direct Addressing Mode

## Slide 8: Direct Addressing Mode
Direct addressing is also used for data transfer between the processor and I/O devices
Example:
  IN 00H is used to receive from port whose address is given in the instruction.
  Similarly, OUT 01 H is used to send data from Accumulator to output port whose address is given in the instruction.

## Slide 9: Register Addressing Mode
In this mode, the operand is in general purpose register named in the instruction.
Transfers a copy of data from the source register to the destination register.
MOV A, B instruction Moves the contents of register B to A.
Very fast

## Slide 10: Register Addressing Mode
Click to add text

## Slide 11: Register Addressing Mode

## Slide 12: Register Indirect Addressing Mode
The address of a memory location is stored in a register and that register is specified in the instruction.
In this mode, the address of operand is specified by a register pair

## Slide 13: Register Indirect Addressing Mode

## Slide 14: Register Indirect Addressing Mode

## Slide 15: Register Indirect Addressing Mode
Other examples are
  ADD M
  ADC M
  INR M
  LDAX Rp
  STAX Rp

## Slide 16: Immediate Addressing Mode
In this mode, the operand is specified within the instruction itself. 8 or 16 bit data can be specified as a part of instruction.
No memory reference to fetch data

## Slide 17: Immediate Addressing Mode

## Slide 18: Implicit Addressing Mode
If address of source of data as well as address of destination of result is fixed, then there is no need to give any operand along with the instruction.
Here, opcode specifies the address of operands

## Slide 19: Implicit Addressing Mode

## Slide 20
Instruction classification based on length

## Slide 21: Instruction classification
Based on length of machine language code, 8085 instructions are classified into
  One byte instructions
  Two byte instructions
  Three byte instructions

## Slide 22: One byte instructions
Requires only one byte in machine language
Examples are
Opcode | Operand | Machine code
MOV | A,B | 78
ADD | M | 86
Example: MOV A, B (coded as 01111000 = 78H)

## Slide 23: Two byte instructions
Requires two bytes in machine code, the first byte is the opcode. The second byte is the 8 bit operand.
Examples are:
Opcode | Operand | Machine code | Byte description
MVI | A, 7FH | 3E 7F | First byte Second byte
ADI | 0FH | C6 0F | First byte Second byte
IN | 40H | DB 40 | First byte Second byte

## Slide 24: Three byte instructions
Requires three bytes in machine code
The first byte is the opcode. The next two bytes refer to the 16 bit operand.
Examples are
Opcode | Operand | Machine code | Byte description
JMP | 9050H | C3 50 90 | First byte Second byte Third byte
LDA | 8850H | 3A 50 88 | First byte Second byte Third byte