## Slide 1: Stack in 8085

## Slide 2: Programmer's view of 8085

## Slide 3: Introduction to Stack
The stack is a reserved area of the memory (identified by the programmer) where we can store temporary information.
The stack is a LIFO structure.
The stack normally grows backwards into memory.

## Slide 4: How does a stack work in assembly language?
The 8085 provides two instructions: PUSH and POP for storing information on the stack and retrieving it back.
– Both PUSH and POP work with register pairs ONLY.

## Slide 5: Operation of the Stack
During pushing, the stack operates in a decrement then store style.
During poping, the stack operates in a use then increment style.
The SP pointer always points to the top of the stack.

## Slide 6: LIFO
The order of PUSHs and POPs must be opposite of each other in order to retrieve information back into its original location.
PUSH B
PUSH D
...
POP D
POP B

## Slide 7: The PUSH Instruction
PUSH B (1 Byte Instruction) Rp
  Decrement SP
  Copy the contents of register B to the memory location pointed to by SP
  Decrement SP
  Copy the contents of register C to the memory location pointed to by SP
B C
F3
12
SP
FFFB FFFC FFFD FFFE FFFF
F3
12

## Slide 8: The POP Instruction
POP D (1 Byte Instruction)
  Copy the contents of the memory location pointed to by the SP to register E
  Increment SP
  Copy the contents of the memory location pointed to by the SP to register D
  Increment SP
F3
12
D
E
SP
FFFB FFFC FFFD FFFE FFFF
F3
12

## Slide 9: Saving Information on the Stack
There are two methods to add data to the stack:
  Direct method
  Indirect method

## Slide 10: Saving Information on the Stack
Direct method
  the stack pointers address is loaded into the stack pointer register directly LXI SP,8000H LXI H,1234H PUSH H POP D HLT

## Slide 11: Saving Information on the Stack
Indirect method
  the stack pointer’s address is loaded into the stack pointer register via another register pair. LXI H,8000H SPHL LXI H,1234H PUSH H POP D HLT

## Slide 12: PSW Register Pair
The 8085 recognizes one additional register pair called the PSW (Program Status Word).
– This register pair is made up of the Accumulator and the Flags registers.
It is possible to push the PSW onto the stack, do whatever operations are needed, then POP it off of the stack.

## Slide 13: PUSH PSW Register Pair
PUSH PSW (1 Byte Instruction)
– Decrement SP
– Copy the contents of register A to the memory location pointed to by SP
– Decrement SP
– Copy the contents of Flag register to the memory location pointed to by SP

## Slide 14: Pop PSW Register Pair
POP PSW (1 Byte Instruction)
– Copy the contents of the memory location pointed to by the SP to Flag register
– Increment SP
– Copy the contents of the memory location pointed to by the SP to register A
– Increment SP

## Slide 15: Modify Flag Content using PUSH/POP
We want to Reset the Zero Flag