## Slide 1: Interferences in Data Communication
National Institute of Technology Rourkela

## Slide 2: What is an interference ?
Performance of a data communication system is greatly influenced by the interference it is subject to during operation.
Degradation happens due to interference resulting in packet drops, retransmissions, link instability and inconsistent protocol behavior.
Mitigating the effect of interference
Evaluation and Avoidance of Interference
Minimum Total node Interference
Modeling Interference
Development of interference aware protocol
Node level interference Vs.Link Level Interference

## Slide 3: Interference Model
Accurate interference models are important for use in trans-mission scheduling algorithms in wireless networks.
The condition for successful reception of packets:
Signal-to-interference-plus-noise ratio (SINR) > a threshold,
Threshold depends on:
the acceptable BER,
Detector structure,
Modulation/demodulation scheme, and
Channel coding/decoding algorithm.
No. of Interferers: Single or Multiple
Pairwise RSS measurement between b/n T & R and I & R
Transmitter-Receiver Distance
Interferer-Receiver Distance
How often base station send the command/poll messages to other sensor nodes
Packet size Ex. 128 Bytes Packet
Noise estimation: By sampling RSS register periodically (Ex. Every 20 ms in a period of 6 s)
Concurrent transmission by Transmitter and Interferer (Packet Reception Rate(PRR) needs to be recorded
PRR (Packet Reception Rate), Number of Sensor Nodes, Throughput, Channel Bandwidth

## Slide 4: Interference Model (Single Interferer)
Graded and Thresholded Physical Interference Model
Assume That
S is the signal power received at the intended receiver from the sender,
N is the noise power at the receiver
I is the interference power of Interferer
ΣI is the sum of the interference powers experienced at the receiver caused by the group of interferers (transmitting concurrently),
BER is the bit error rate
The model predicts the relationship between the bit error rate (BER) and SINR,
where SINR = S/(ΣI + N)
This relationship depends on radio properties such as modulation.
The packet error rate (PER) is directly related to BER and depends on coding.
The packet reception rate (PRR) = 1 − PER.
SINR = S/(I+N)

## Slide 5: Multiple Interference Model
Assume that r, s and I denote a nodes or devices in a data communication system
RSS(p,r,s) the received signal strength at node r when a node s transmits with transmit power p
Nr the ambient noise at r.
S is the set of sensor nodes
PRR at r from a node i ∈ S as PRR(p, r, i, S). (can be meausered directly)
Assume that a set of nodes, S, is active simultaneously transmitting at power p.
The SINR at r for node i is given by
SINR(p, r, i, S) = RSS(p, r, i) / (Nr + Σ RSS(p, r, j) ∀ j ∈ S, j is not = to i

## Slide 6: References
Ritesh Maheshwari, Shweta Jain, Samir R. Das, A Measurement Study of Interference Modeling and Scheduling in Low-Power Wireless Networks, Proceedings of the 6th International Conference on Embedded Networked Sensor Systems, SenSys 2008, Raleigh, NC, USA, November 5-7, 2008

## Slide 7
Thank You